BINAC Description

Note that the second column of mnemonics is mine.

Order	Mnemonics		Description	uSecs
01	STOP	HLT	Stop computer	N/A
02	F(m)	ADL	Add L register to A register	123
03	D(m)	DIV m	Divide A by the contents of memory location m, put the result in A rounded to 30 binary digits. Contents of L are lost (probably cleared but should not be assumed)	633
04	C(m)	STC m	Transfer A to memory location m, and clear A	285
05	A(m)	ADD m	Add the contents of memory location m to A	285
10	M(m)	MUL m	Multiply A by the contents of memory A, rounded to 30 binary digits, Contents of L are lost (probably cleared but should not be assumed)	654
11	K(m)	TLC	Transfer A to L, and Clear A	123
12	L(m)	TAL	Transfer A to L	123
13	H(m)	STA m	Transfer A to memory location A.	285
14	T(m)	BMI m	If A is negative, then set the program counter to m ; clear Accumulator in either case. Note that instructions are in pairs in each word.	123
15	S(m)	SUB m	Subtract the contents of memory location m from A	285
20	U(m)	BRA m	Set the program counter to m.	123
22	+(m)	SHL	Shift A left, losing the sign digit	123
23	-(m)	SHR	Shift A right, preserving the sign digit.	123
24	BP(m)	HBR	Stop if the break point switch is set	123
25	SKIP	NOP	Do nothing (used for padding unused instruction space if a branch is the first instruction in a word, amongst others)	123

Registers

31 bit Accumulator	'A'
31 bit auxiliary register	'L' (contains multiplicand/divisor during those arithmetic instructions)
9 bit program counter	'Memory Position Counter'

The packing is shown (albeit backwards !) in Fig 1 of Auerbach.

30 Sign	29 MSD	28-24	23-15	14	13-9	8-0
Unused	Unused	Order 1	Address 1	Unused	Order 2	Address 2